## Slide 1: SYNTAX

## Slide 2: Similar to C programming(pls revise)
Functions
For, while loops, if else statements
Semicolon to signify end of statement
//comments
Variables – declaration, scope, type
Arrays
Operations- arithmetic, logical, comparison, Boolean

## Slide 3: Formatting rules
All Sketches need to contain one “void setup(){}” and one “void loop(){}”
“{“and “}” indicate the beginning and end of a function (think void loop and setup) or conditions (if, else, if else). These are VERY IMPORTANT
“;” is placed after most lines, except the if, else conditions
Correct SPELLING is very important. If spelling varies, the sketch assumes we are talking about different entities and gives an error
Verify, on errors, shows the line around which the error exists and what the error is.
“//” comments or tells the IDE to ignore what is in that one line and “/* and */” tells the Arduino to ignore everything between these symbols, code be paras of code. All will be ignored

## Slide 4: Basic structure
The basic structure of Arduino programming language runs in atleast two parts, or functions that enclose blocks of statements
void setup()
{ <statements>
}
void loop
{
<statements>
}

## Slide 5: setup()
The setup() function is called once when your program starts. Use it to initialize pin modes, or begin serial. It must be included in the program even if there are no statements to run.
void setup()
{ pinMode(13, OUTPUT); //set pin 13 as output
}

## Slide 6: loop()
After calling setup() function, loop() function is run continuously over and over.
void loop()
{ digitalWrite(13, HIGH); //set pin 13 to HIGH
delay(1000); //wait for 1000ms
digitalWrite(13,LOW);
delay(1000);

## Slide 7: Declaring input/output
Each digital and analog pin is assigned a number
For any pin to be used, the mode has to be assigned as either INPUT or OUTPUT
Done using pinMode() function
pinMode(pin number, mode)
Eg. pinMode(13, OUTPUT)
Here pin 13 is defined as output.

## Slide 8: Pin levels
HIGH and LOW are either read or written to digital pins
HIGH =1
LOW =0
Function used to write is digitalWrite
digitalWrite(pin number, LEVEL)
Eg. digitalWrite(13,LOW)
Makes output of pin 13 LOW

## Slide 9: Other inbuilt functions
digitalRead(pin)
analogWrite(pin, value)
analogRead(pin)
delay(ms)

## Slide 10: Serial port
Data of sensors is sent through serial port
To view data, click on magnifying glass at the right top of IDE
In setup()
Serial.begin(rate) – opens serial port and sets the baud rate for serial data transmission(typically 9600 bps)
In loop()
Serial.println(data) – prints data to serial port